## Slide 1: ELEC 522 Project 2
Aedan Cullen

## Slide 2
Processing element design

## Slide 3
Array organization

## Slide 4
Pipelining
Each processing element performs multiply and accumulate in parallel each cycle.
Multipliers are pipelined with latency 2.
9 clock cycles are needed from the time the first elements are shifted in to the time the first complete column of the result is ready.
Resource utilization
16 DSPs, 495 LUTs, 832 registers
Maximum clock frequency
~364 MHz (2.75 ns clock period)